## Slide 1
<number>
For ‘Rule of 10s and 3s Example 3’ you will use some more complex calculations. The access point is transmitting at 50 mW. The signal loss between the access point and the antenna is 1 dB, and the antenna provides 5 dBi of gain.

## Slide 2
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
1
Start off with the template.
0
1
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 3
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
1
10
100
50
You need to determine if by using
* and ÷, and 2 and 10, you can change from 1 to 50 mW.
*10
*10
÷2
You determine that by multiplying
1 by 10 twice, and then dividing by 2 you will get 50 mW. Calculate the new mW value by performing all of these calculations, and enter the new values in the mW column.
0
1
*10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 4
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
1
10
100
50
*10
*10
÷2
Remember that whatever you do to one side, you must do the correlative mathematics on the other side. Since you multiplied by 10 twice on the right side, you must add 10 twice on the left. And since you divided by 2 on the right, you must subtract 3 on the left.
+10
+10
-3
0
1
*10
+10
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 5
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
1
10
100
50
When using more complex calculations, it is often easier to put a line between the different calculations and label each group.
*10
*10
÷2
+10
+10
-3
0
1
*10
+10
Access
Point
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 6
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
7
10
13
16
1
10
100
50
The next thing you need to do is calculate the 1 dB connector loss. Table 3.3 in the book showed you that -1 dB can be calculated using -10 + 3 + 3 + 3.
*10
*10
÷2
+10
+10
-3
-10
+3
+3
+3
Access
Point
Connector
loss
0
1
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 7
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
7
10
13
16
1
10
100
50
5
10
20
40
*10
*10
÷2
÷10
*2
*2
*2
Again, whatever you do to one side, you must do the correlative mathematics on the other side. Since you subtracted 10 on the left, you must divide by 10 on the right. And since you added 3 three times on the left, you must multiply by 2 three times on the right. So the IR is either 16 dBm or 40 mW.
+10
+10
-3
-10
+3
+3
+3
Access
Point
Connector
loss
0
1
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 8
<number>
dBm
mW
+
-
*
÷
3
10
10
2
The next step is to increase the dBm side by the 5 dBi of the antenna. Table 3.3 shows that +5 is equal to
+ 10 + 10 - 3 - 3 - 3 - 3 - 3
0
10
20
17
7
10
13
16
26
36
33
30
27
24
21
1
10
100
50
5
10
20
40
*10
*10
÷2
÷10
*2
*2
*2
+10
+10
-3
-10
+3
+3
+3
+10
+10
-3
-3
-3
-3
-3
Access
Point
Connector
loss
Antenna
0
1
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 9
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
7
10
13
16
26
36
33
30
27
24
21
1
10
100
50
5
10
20
40
400
4000
2000
1000
500
250
125
*10
*10
÷2
÷10
*2
*2
*2
*10
*10
÷2
÷2
÷2
÷2
÷2
+10
+10
-3
-10
+3
+3
+3
+10
+10
-3
-3
-3
-3
-3
Access
Point
Connector
loss
Antenna
The last step is to perform the correlative mathematical commands on the mW column.
0
1
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain

## Slide 10
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
7
10
13
16
26
36
33
30
27
24
21
1
10
100
50
5
10
20
40
400
4000
2000
1000
500
250
125
*10
*10
÷2
÷10
*2
*2
*2
*10
*10
÷2
÷2
÷2
÷2
÷2
+10
+10
-3
-10
+3
+3
+3
+10
+10
-3
-3
-3
-3
-3
Access
Point
Connector
loss
Antenna
So the EIRP is either
21 dBm or
125 mW
0
1
*10
+10
Rule of 10s and 3s Example 3: 50 mW access point, 1 dB connector loss, 5 dBi antenna gain