## Slide 1
<number>
For review question 10, you have a wireless bridge generating a 100 mW signal. The antenna cable and connectors create 3 dB of signal loss, and the antenna provides 16 dBi of gain.

## Slide 2
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
1
Start off with the template.
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 3
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
1
=10
=100
You need to determine if by using * and ÷ and 2 and 10, you can change from 1 to 100 mW.
*10
*10
You determine that by multiplying 1 by 10 twice, you will get 100 mW. Calculate the new mW value by performing both of these multiplications, and enter the new values in the mW column.
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 4
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
=10
=20
1
10
100
*10
*10
Remember that whatever you do to one side, you must do the correlative mathematics on the other side. Since you multiplied on the right side, you must add on the left. And since you multiplied by 10 twice on the right, you must add 10 twice on the left.
+10
+10
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 5
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
=17
1
10
100
Subtract 3 for the cable loss.
*10
*10
+10
+10
-3
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 6
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
1
10
100
=50
*10
*10
÷2
Again, whatever you do to one side, you must do the correlative mathematics on the other side. Since you subtracted on the left, you must divide on the right. And since you subtracted 3 on the left, you must divide by 2 on the right.
+10
+10
-3
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 7
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
=27
=30
=33
1
10
100
50
*10
*10
÷2
All that’s left is to include the effects of the antenna. To do this, you must increase the dBm side by the 16 dBi of the antenna. To accomplish this, you need to add on 10 and two 3s.
+10
+10
-3
+10
+3
+3
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 8
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
27
30
33
1
10
100
50
=500
=1000
=2000
*10
*10
÷2
*10
*2
*2
Now you need to perform the correlative calculations to the mW side. So you must multiply by one 10 and two 2s.
+10
+10
-3
+10
+3
+3
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain

## Slide 9
<number>
dBm
mW
+
-
*
÷
3
10
10
2
0
10
20
17
27
30
33
1
10
100
50
500
1000
2000
*10
*10
÷2
*10
*2
*2
So the EIRP is 33 dBm or 2000 mW (2 W).
+10
+10
-3
+10
+3
+3
Review question 10: 100 mW bridge, 3 dB cable loss, 16 dBi antenna gain